## Slide 1: Layout titolo
Sottotitolo

## Slide 3: What we wanted it to be:
Something that actually moves around without catching fire
  (it actually catched fire at some point)
Something that can be controlled remotely
Something that somehow perceives it’s proximities

## Slide 4: CM-01 Automatic Car
What we wanted it to be:
Something that actually moves around without catching fire
  (it actually catched fire at some point)
Something that can be controlled remotely
Something that somehow perceives it’s proximities
What we achieved:
Mobility: 4 wheels, controlled in pairs
Remote Control:
  Wifi: using ESP8266
  Infrared remote
Proximity sensing:
  HCSR04 ultrasonic range sensor + servo for scanning at 180°
  IR range sensor for line following

## Slide 5: Components:
DC motors + Wheels:
  Sold in couples, 5 euros on Amazon, much less on Aliexpress.
  Rated 3V – 6V

## Slide 6: Components:
Arduino Mega 2560 REV3
  Has LOTS of GPIO pins, PWM-enabled pins and Analog pins
  Multiple Serial interfaces
  Same layout of Arduino Uno for shield compatibility

## Slide 7: Components:
2x 18650 Li-ion cells
  3.6V each (actually almost 4V when fully charged)
  !!Faulty battery socket can make them catch fire!!
    But as long as you’re careful it should be ok

## Slide 8: Components:
Voltage meter:
  Small
  Not very accurate but it’s used only for battery charge status estimation

## Slide 9: Components:
ESP-13 shield
  Carries an ESP-WROOM-02 module based on ESP8266
  Not mounted as a shield (going to see why soon)
  Cheap compared to other ESP8266 shields
    Turns out there’s a reason for that

## Slide 10: Components:
5X IR proximity sensing modules
  Contains an LML393 comparator by ON Semiconductor coupled with a TRT5000 sensor by Vishay
  Functioning explained later
  Used to let the car follow a black line on the terrain

## Slide 11: Components:
Piezo Active Buzzer Module
  Rated for 3.3V-5V (transistor onboard for power mode switching)
  Different from passive buzzer:
    Can generate a fixed tone when I/O is HIGH (3.3V)
    Con: no frequency control
    Pro: doesn’t require a pre-generated waveform

## Slide 12: Components:
IR receiver module
  Basically a TL1838 Infrared Receiver mounted on a pcb + LED to signal incoming IR message
  Allows car to receive signals from any el-cheapo IR transmitter or remote control

## Slide 13: Components:
HCSR04 Ultrasonic Ranging Module:
  A couple of transducers, one for transmitting and one for receiving are used to measure an echo delay, thus estimating a linear distance from the sensor itself.
  Mounted on a rotating support ot scan multiple directions
  Kinda makes the whole thing look like Wall-E

## Slide 14: Components:
Jumper Wires
  Everything is connected using jumper wires:
    MtF
    MtM
    FtF

## Slide 15: Components:
Piezo Active Buzzer Module
  Rated for 3.3V-5V (transistor onboard for power mode switching)
  Different from

## Slide 16: Schematics

## Slide 17: Putting everything together:
The ESP shield

## Slide 18
The ESP shield
The ESP-13 is an Arduino Uno shield whith an embedded ESP-WROOM02 module.
The ESP-WROOM02 by Espressif is an integrated WiFi 802.11 b/g/n module designed for providing wireless connection to embedded systems, it’s powered by an ESP8266EX chip, a 32 bit low-power microcontroller, with 2MB of onboard memory and can be programmed with the Arduino IDE.
ESP-13 by Jaycar offers a breakout for all the pins of the ESP-WROOM02, an onboard voltage divider for powering the ESP-WROOM02 itself (Arduino offers a 5V line but ESP8266 uses 3.3V signals both for powering and GPIO communication) and a level shifter for the logic signals coming from and to the Arduino.
Or at least it should…

## Slide 19: Layout titolo e contenuto con grafico
Chart: 
| Categoria 1 | Categoria 2 | Categoria 3 | Categoria 4
Serie 1 | 4.3 | 2.5 | 3.5 | 4.5
Serie 2 | 2.4 | 4.4 | 1.8 | 2.8
Serie 3 | 2 | 2 | 3 | 5

## Slide 20: Layout due contenuti con tabella
Primo punto elenco qui
Secondo punto elenco qui
Terzo punto elenco qui
Classe | Gruppo 1 | Gruppo 2
Classe 1 | 82 | 95
Classe 2 | 76 | 88
Classe 3 | 84 | 90

## Slide 21: Layout titolo e contenuto con SmartArt
Titolo fase 1
Descrizione attività
Titolo fase 2
Descrizione attività
Titolo fase 3
Descrizione attività

## Slide 22: Aggiungere un titolo di diapositiva - 1

## Slide 23: Aggiungere un titolo di diapositiva - 2

## Slide 24: Aggiungere un titolo di diapositiva - 3

## Slide 26: Aggiungere un titolo di diapositiva - 4

## Slide 27: Aggiungere un titolo di diapositiva - 5