## Slide 1: Layout titolo
Sottotitolo

## Slide 3: What we wanted it to be:
Something that actually moves around without catching fire
  (it actually catched fire at some point)
Something that can be controlled remotely
Something that somehow perceives it’s proximities

## Slide 4: CM-01 Automatic Car
What we wanted it to be:
Something that actually moves around without catching fire
  (it actually catched fire at some point)
Something that can be controlled remotely
Something that somehow perceives it’s proximities
What we achieved:
Mobility: 4 wheels, controlled in pairs
Remote Control:
  Wifi: using ESP8266
  Infrared remote
Proximity sensing:
  HCSR04 ultrasonic range sensor + servo for scanning at 180°
  IR range sensor for line following

## Slide 5: Components:
DC motors + Wheels:
  Sold in couples, 5 euros on Amazon, much less on Aliexpress.
  Rated 3V – 6V

## Slide 6: Components:
Arduino Mega 2560 REV3
  Has LOTS of GPIO pins, PWM-enabled pins and Analog pins
  Multiple Serial interfaces
  Same layout of Arduino Uno for shield compatibility

## Slide 7: Components:
2x 18650 Li-ion cells
  3.6V each (actually almost 4V when fully charged)
  !!Faulty battery socket can make them catch fire!!
    But as long as you’re careful it should be ok

## Slide 8: Components:
Voltage meter:
  Small
  Not very accurate but it’s used only for battery charge status estimation

## Slide 9: Components:
ESP-13 shield
  Carries an ESP-WROOM-02 module based on ESP8266
  Not mounted as a shield (going to see why soon)
  Cheap compared to other ESP8266 shields
    Turns out there’s a reason for that

## Slide 10: Components:
5X IR proximity sensing modules
  Contains an LML393 comparator by ON Semiconductor coupled with a TRT5000 sensor by Vishay
  Functioning explained later
  Used to let the car follow a black line on the terrain

## Slide 11: Components:
Piezo Active Buzzer Module
  Rated for 3.3V-5V (transistor onboard for power mode switching)
  Different from passive buzzer:
    Can generate a fixed tone when I/O is HIGH (3.3V)
    Con: no frequency control
    Pro: doesn’t require a pre-generated waveform

## Slide 12: Components:
IR receiver module
  Basically a TL1838 Infrared Receiver mounted on a pcb + LED to signal incoming IR message
  Allows car to receive signals from any el-cheapo IR transmitter or remote control

## Slide 13: Components:
HCSR04 Ultrasonic Ranging Module:
  A couple of transducers, one for transmitting and one for receiving are used to measure an echo delay, thus estimating a linear distance from the sensor itself.
  Mounted on a rotating support ot scan multiple directions
  Kinda makes the whole thing look like the Curiosity rover

## Slide 14: Components:
Jumper Wires
  Everything is connected using jumper wires:
    MtF
    MtM
    FtF

## Slide 15: Components:
Piezo Active Buzzer Module
  Rated for 3.3V-5V (transistor onboard for power mode switching)
  Different from

## Slide 16: Schematics

## Slide 17: Putting everything together:
The ESP shield
(odissey)

## Slide 18
The ESP shield
The ESP-13 is an Arduino Uno shield whith an embedded ESP-WROOM02 module.
The ESP-WROOM02 by Espressif is an integrated WiFi 802.11 b/g/n module designed for providing wireless connection to embedded systems, it’s powered by an ESP8266EX chip, a 32 bit low-power microcontroller, with 2MB of onboard memory and can be programmed with the Arduino IDE.
ESP-13 by Jaycar offers a breakout for all the pins of the ESP-WROOM02, an onboard voltage divider for powering the ESP-WROOM02 itself (Arduino offers a 5V line but ESP8266 uses 3.3V signals both for powering and GPIO communication) and a level shifter for the logic signals coming from and to the Arduino.
Or at least it should…

## Slide 19
The ESP shield
The RX and TX pins on the shield, corresponding to the pins 0 (RX) and 1 (TX) in the Arduino layout were actually switched, rendering impossible to use the shield in it’s intended configuration.
RX
TX
RX0
TX0
RX
TX
RX0
TX0

## Slide 20
The ESP shield
Possible solutions:
Trash the whole thing
  Tempting but not very cost-effective
Fix the onboard traces
    Scrape the soldermask to expose the traces
    cut the traces in two different points
    run two jumper wires
  Time-consuming
  I didn’t have any small-diameter wire laying around that day
Just connect it using jumper wires
  Lazy solution
  Automatically best solution

## Slide 21
The ESP shield
RX 1 > TX0
TX 1 > RX0
5V > 5V
GND > GND

## Slide 22
The ESP shield
5V (ARDUINO)
3.3V
(ESP8266)
The onboard voltage regulator should convert the 5V power provided by arduino and convert it to a 3.3V line that can be used by the ESP8266
BUT WAIT
The serial lines on the ESP8266 should also use 3.3V logic: we need a level shifter so that 5V signals from the Arduino can be translated to 3.3V for the ESP8266 and vice versa.
or do we?

## Slide 23
The ESP shield
I remembered seeing some years a go a post on hackaday.com discussing wether the ESP8266 was actually 5V tolerant: people were using the ESP8266 serial lines with 5V logic without consequences
Didn’t remember the post saying anything definitive at the time, but just for the sake of it I decided to look back.

## Slide 24
The ESP shield
With the benediction of the Espressif CEO I could finally lazily connect my ESP8266 to 5V logic without any remorse

## Slide 25
The ESP shield
Ok, that looks good, can we finally use the ESP8266?
nope
To be programmed using the Arduino IDE, the ESP8266 needs the AT Firmware by Espressif
Turns out the ESP8266 came pre-flashed with the chinese DOIT firmware

## Slide 26
The ESP shield
It’s not a bad firmware per-se, but it does only one thing (and actually does it well):
Configures the ESP8266 to act as an access point
Starts a webserver on 192.168.4.1 and streams a nice config page from there
Listens on the serial connection
Encapsules every received sequence in a TCP package and streams it on the webserver.
But that’s not what we need!

## Slide 27
The ESP shield
turn right!
turn right!
* turns right *
DOIT configuration
our configuration

## Slide 28
The ESP shield
We need to flash the AT firmware:
It can be downloaded from the Espressif website at www.espressif.com along with the firmware flashing tool: easy peasy no?
kinda...

## Slide 29
The ESP shield
How do we connect the ESP8266 to the pc?
The ESP-WROOM02 doesn’t have it’s own USB-UART hardware like the Arduino so it needs some kind of USB-TTL interface to be programmed, they’re quite cheap to purchase on any online shop...
...but we’re both broke and lazy.
We can use what we already have: Arduinos!
Arduino has it’s own USB-TTL interface to program the onboard Atmel ATMEGA328P, we can use that instead of purchasing a USB-TTL adapter.
How to use what we have?

## Slide 30
The ESP shield
How do we connect the ESP8266 to the pc?
Let’s take a look at the Arduino uno schematics:
This is clearly power-related stuff we don’t care for...
These are the interesting parts:
The ATMEGA controller
The USB-TTL adapter

## Slide 31
The ESP shield
How do we connect the ESP8266 to the pc?
The D+ and D- differential data lines reach the USB-TTL interface:
we can then decide to program the chip either through an ICSP interface or a simple RX/TX coupl

## Slide 32
The ESP shield
How do we connect the ESP8266 to the pc?
The PD0 and PD1 pins of the ATMEGA328P are exposed as pin 0 and 1 on the Arduino board!
That solves part of our economical problems as we probably won’t have to but a USB-TTL adapter!

## Slide 33
The ESP shield
How do we connect the ESP8266 to the pc?
Method 1: The Literal No-brainer
We now need a practical method to adapt the USB-TTL interface to our needs:
Remove the ATMEGA328P from it’s socket
Power up the ESP8266 connecting the 3.3V line to the Arduino 5V through the voltage regulator as we did before
Connect the RX and TX pins of the ESP8266 to the Arduino
  We’re not trying to communicate with a the arduino but are trying to talk directly to the USB-TTL chip, the right connection scheme now is RX0 -> RX, TX0 -> TX!
That looks good if we have a socketed controller line in the Uno case, but what about the Mega?

## Slide 34
The ESP shield
How do we connect the ESP8266 to the pc?
Method 2: The Sleeping Beauty
Run a jumper wire between RESET and GND
Proceed exactly as Method 1
The Mega has a soldered ATMEGA2560 controller that might be little bit impractical to remove.
If we can’t remove the controller itself we can just silence it when we need to speak with the ESP8266 by grounding it’s reset signal.

## Slide 35
The ESP shield
You got to find

## Slide 36: Layout titolo e contenuto con grafico
Chart: 
| Categoria 1 | Categoria 2 | Categoria 3 | Categoria 4
Serie 1 | 4.3 | 2.5 | 3.5 | 4.5
Serie 2 | 2.4 | 4.4 | 1.8 | 2.8
Serie 3 | 2 | 2 | 3 | 5

## Slide 37: Layout due contenuti con tabella
Primo punto elenco qui
Secondo punto elenco qui
Terzo punto elenco qui
Classe | Gruppo 1 | Gruppo 2
Classe 1 | 82 | 95
Classe 2 | 76 | 88
Classe 3 | 84 | 90

## Slide 38: Layout titolo e contenuto con SmartArt
Titolo fase 1
Descrizione attività
Titolo fase 2
Descrizione attività
Titolo fase 3
Descrizione attività

## Slide 39: Aggiungere un titolo di diapositiva - 1

## Slide 40: Aggiungere un titolo di diapositiva - 2

## Slide 41: Aggiungere un titolo di diapositiva - 3

## Slide 43: Aggiungere un titolo di diapositiva - 4

## Slide 44: Aggiungere un titolo di diapositiva - 5