## Slide 1: Uolli
A tale of software bugs and fried hardware
https://github.com/filippocastelli/uolli
Bologna, 21/12/2018

## Slide 2: CM-01 Automatic Car
What we wanted it to be:
Something that actually moves around without catching fire
  (it actually catched fire at some point)
Something that can be controlled remotely
Something that somehow perceives it’s proximities
What we achieved:
Mobility: 4 wheels, controlled in pairs
Remote Control:
  Wifi: using ESP8266
  Infrared remote
Proximity sensing:
  HCSR04 ultrasonic range sensor + servo for scanning at 180°
  IR range sensor for line following

## Slide 3: Components:
DC motors + Wheels:
  Sold in couples, 5 euros on Amazon, much less on Aliexpress.
  Rated 3V – 6V

## Slide 4: Components:
Arduino Mega 2560 REV3
  Has LOTS of GPIO pins, PWM-enabled pins and Analog pins
  Multiple Serial interfaces
  Same layout of Arduino Uno for shield compatibility

## Slide 5: Components:
2x 18650 Li-ion cells
  3.6V each (actually almost 4V when fully charged)
  !!Faulty battery socket can make them catch fire!!
    But as long as you’re careful it should be ok

## Slide 6: Components:
Voltage meter:
  Small
  Not very accurate but it’s used only for battery charge status estimation

## Slide 7: Components:
ESP-13 shield
  Carries an ESP-WROOM-02 module based on ESP8266
  Not mounted as a shield (going to see why soon)
  Cheap compared to other ESP8266 shields
    Turns out there’s a reason for that

## Slide 8: Components:
5X IR proximity sensing modules
  Contains an LML393 comparator by ON Semiconductor coupled with a TRT5000 sensor by Vishay
  Functioning explained later
  Used to let the car follow a black line on the terrain

## Slide 9: Components:
Piezo Active Buzzer Module
  Rated for 3.3V-5V (transistor onboard for power mode switching)
  Different from passive buzzer:
    Can generate a fixed tone when I/O is HIGH (3.3V)
    Con: no frequency control
    Pro: doesn’t require a pre-generated waveform

## Slide 10: Components:
IR receiver module
  Basically a TL1838 Infrared Receiver mounted on a pcb + LED to signal incoming IR message
  Allows car to receive signals from any el-cheapo IR transmitter or remote control

## Slide 11: Components:
HCSR04 Ultrasonic Ranging Module:
  A couple of transducers, one for transmitting and one for receiving are used to measure an echo delay, thus estimating a linear distance from the sensor itself.
  Mounted on a rotating support ot scan multiple directions
  Kinda makes the whole thing look like the Curiosity rover

## Slide 12: Components:
Jumper Wires
  Everything is connected using jumper wires:
    MtF
    MtM
    FtF

## Slide 13: Components:
Piezo Active Buzzer Module
  Rated for 3.3V-5V (transistor onboard for power mode switching)
  Different from

## Slide 14: Schematics

## Slide 15: Putting everything together:
The ESP-13 shield
(odissey)

## Slide 16
The ESP shield
The ESP-13 is an Arduino Uno shield whith an embedded ESP-WROOM02 module.
The ESP-WROOM02 by Espressif is an integrated WiFi 802.11 b/g/n module designed for providing wireless connection to embedded systems, it’s powered by an ESP8266EX chip, a 32 bit low-power microcontroller, with 2MB of onboard memory and can be programmed with the Arduino IDE.
ESP-13 by Jaycar offers a breakout for all the pins of the ESP-WROOM02, an onboard voltage divider for powering the ESP-WROOM02 itself (Arduino offers a 5V line but ESP8266 uses 3.3V signals both for powering and GPIO communication) and a level shifter for the logic signals coming from and to the Arduino.
Or at least it should…

## Slide 17
The ESP shield
The RX and TX pins on the shield, corresponding to the pins 0 (RX) and 1 (TX) in the Arduino layout were actually switched, rendering impossible to use the shield in it’s intended configuration.
RX
TX
RX0
TX0
RX
TX
RX0
TX0

## Slide 18
The ESP shield
Possible solutions:
Trash the whole thing
  Tempting but not very cost-effective
Fix the onboard traces
    Scrape the soldermask to expose the traces
    cut the traces in two different points
    run two jumper wires
  Time-consuming
  I didn’t have any small-diameter wire laying around that day
Just connect it using jumper wires
  Lazy solution
  Automatically best solution

## Slide 19
The ESP shield
RX 1 > TX0
TX 1 > RX0
5V > 5V
GND > GND

## Slide 20
The ESP shield
5V (ARDUINO)
3.3V
(ESP8266)
The onboard voltage regulator should convert the 5V power provided by arduino and convert it to a 3.3V line that can be used by the ESP8266
BUT WAIT
The serial lines on the ESP8266 should also use 3.3V logic: we need a level shifter so that 5V signals from the Arduino can be translated to 3.3V for the ESP8266 and vice versa.
or do we?

## Slide 21
The ESP shield
I remembered seeing some years a go a post on hackaday.com discussing wether the ESP8266 was actually 5V tolerant: people were using the ESP8266 serial lines with 5V logic without consequences
Didn’t remember the post saying anything definitive at the time, but just for the sake of it I decided to look back.

## Slide 22
The ESP shield
With the benediction of the Espressif CEO I could finally lazily connect my ESP8266 to 5V logic without any remorse

## Slide 23
The ESP shield
Ok, that looks good, can we finally use the ESP8266?
nope
To be programmed using the Arduino IDE, the ESP8266 needs the AT Firmware by Espressif
Turns out the ESP8266 came pre-flashed with the chinese DOIT firmware

## Slide 24
The ESP shield
It’s not a bad firmware per-se, but it does only one thing (and actually does it well):
Configures the ESP8266 to act as an access point
Starts a webserver on 192.168.4.1 and streams a nice config page from there
Listens on the serial connection
Encapsules every received sequence in a TCP package and streams it on the webserver.
But that’s not what we need!

## Slide 25
The ESP shield
turn right!
turn right!
* turns right *
DOIT configuration
our configuration

## Slide 26
The ESP shield
We need to flash the AT firmware:
It can be downloaded from the Espressif website at www.espressif.com along with the firmware flashing tool: easy peasy no?
kinda...

## Slide 27
The ESP shield
How do we connect the ESP8266 to the pc?
The ESP-WROOM02 doesn’t have it’s own USB-UART hardware, like the Arduino has, so it needs some kind of USB-TTL interface to be programmed, they’re quite cheap to purchase on any online shop...
...but we’re both broke and lazy.
We can use what we already have: Arduinos!
Arduino has it’s own USB-TTL interface to program the onboard Atmel ATMEGA328P, we can use that instead of purchasing a USB-TTL adapter.
How to use what we have?

## Slide 28
The ESP shield
How do we connect the ESP8266 to the pc?
Let’s take a look at the Arduino uno schematics:
This is clearly power-related stuff we don’t care for...
These are the interesting parts:
The ATMEGA controller
The USB-TTL adapter

## Slide 29
The ESP shield
How do we connect the ESP8266 to the pc?
The D+ and D- differential data lines reach the USB-TTL interface:
we can then decide to program the chip talking via the ISP programmer or using the serial, interacting with the ATMEGA328P’s bootloader

## Slide 30
The ESP shield
How do we connect the ESP8266 to the pc?
The PD0 and PD1 pins of the ATMEGA328P are exposed as pin 0 and 1 on the Arduino board!
That solves part of our economical problems as we probably won’t have to buy a USB-TTL adapter!
The ESP8266 can be flashed from serial:
when the GPIO0 pin is held on LOW(GND) it will execute a serial bootloader which will receive the programs we want to flash from the Espressif Flash Tool.

## Slide 31
The ESP shield
How do we connect the ESP8266 to the pc?
Method 1: The Literal No-brainer
We now need a practical method to adapt the USB-TTL interface to our needs:
Remove the ATMEGA328P from it’s socket
Power up the ESP8266 connecting the 3.3V line to the Arduino 5V through the voltage regulator as we did before
Connect the RX and TX pins of the ESP8266 to the Arduino
  We’re not trying to communicate with a the arduino but are trying to talk directly to the USB-TTL chip, the right connection scheme now is RX0 -> RX, TX0 -> TX!
That looks good if we have a socketed controller line in the Uno case, but what about the Mega?

## Slide 32
The ESP shield
How do we connect the ESP8266 to the pc?
Method 2: The Sleeping Beauty
Run a jumper wire between RESET and GND
Proceed exactly as Method 1
The Mega has a soldered ATMEGA2560 controller that might be little bit impractical to remove.
If we can’t remove the controller itself we can just silence it when we need to speak with the ESP8266 by grounding it’s reset signal.

## Slide 33
The ESP shield
Now we can finally proceed to flash the AT firmware on the ESP-WROOM02.
The AT firmware comes with a bunch of files to be flashed at different positions in the memory map

## Slide 34
The ESP shield
The documentation by Espressif helps to choose which .bin is flashed to which memory address as memory can be organized differently from package to package

## Slide 35
The ESP shield
Just define your memory map flashing schedule and a few parameters like
the communication port you’re using
the baud rate
various characteristics of the ESP8266 package can be detected automatically by the tool
it can take a while to figure out the correct settings and the correct firmware version to use for your specific chip.

## Slide 36
The ESP shield
If the firmware is flashed correctly, when sending the command AT+GMR? on serial the ESP8266 should reply with the current firmware version.
Using serial commands you can change settings without needing to reflash a program everytime.

## Slide 37
The ESP shield
We can now develop a program for the ESP8266 module directly in the Arduino IDE! (it requires some extensions available on the Arduino website) using the same C++ language you use for normal Arduino programming:
We set up a webserver wich streams a simple webpage which we use to control the car.
To flash your program you just need the same setup we used to flash the firmware (Arduino IDE only flashes a memory region allocated to program execution).

## Slide 38
The ESP shield
We can now develop a program for the ESP8266 module directly in the Arduino IDE! (it requires some extensions available on the Arduino website) using the same C++ language you use for normal Arduino programming:
We set up a webserver wich streams a simple webpage which we use to control the car.
To flash your program you just need the same setup we used to flash the firmware (Arduino IDE only flashes a memory region allocated to program execution).

## Slide 39
The ESP shield
We can now develop a program for the ESP8266 module directly in the Arduino IDE! (it requires some extensions available on the Arduino website) using the same C++ language you use for normal Arduino programming:
We set up a webserver wich streams a simple webpage which we use to control the car.
To flash your program you just need the same setup we used to flash the firmware (Arduino IDE only flashes a memory region allocated to program execution).

## Slide 40: Putting everything together:
The Software
https://github.com/filippocastelli/uolli

## Slide 41
The Software
We tried to keep things as simple as reasonably possible, so we decided to cut down all the software paraphernalia to only a single tool:
The Arduino IDE can be found on
www.arduino.cc/en/main/software
pre-compiled for a variety of platforms and it’s the ideally the only thing you need to start programming on the Arduino platform.
The Arduino IDE

## Slide 42
The Software
You don’t even need to install it to start coding! You can use a web-based Arduino Create! IDE available on the Arduino webpage.
https://create.arduino.cc/editor
Arduino Create!

## Slide 43
The Software
Arduino can be programmed in a special C / C++ dialect that requires absolutely 0 learning effort if you’ve already programmed in C/C++
https://www.arduino.cc/en/tutorial/sketch
Anatomy of and Arduino Sketch:
As a matter of fact every time that you compile an Arduino Sketch it’s actually translated to C/C++ code and compiled using the AVR version of the g++ compiler with the compiler we’re all familiar with, called avr-g++

## Slide 44
The Software
Any sketch has to implement at least two functions:
https://www.arduino.cc/en/tutorial/sketch
Anatomy of and Arduino Sketch:
the setup() function:
  I’s the first part of the program and it’s called only once when the Arduino wakes up.
the loop() function:
  as the name suggests it’s looped over and over until the thermodynamic death of the universe
You may want to use setup() for setting up all you need in terms of IO pin settings and then run the actual program in loop()

## Slide 45
The Software
You can also divide your code and function definitions in multiple files without caring for linking as long as:
The main sketch has the same name of the directory it’s in
The other files are in the same directory
https://www.arduino.cc/en/tutorial/sketch
Anatomy of and Arduino Sketch:

## Slide 46
The Software
The main file is extremely simple:
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
Just some imports for IRremote.h, Servo.h and our configuration file conf.h
In the setup() we call specific setup routines we’ve written for everything we need and open two serial connections
One on TX0,RX0 for usb debugging
One on TX1, RX1 for communication with the ESP8266

## Slide 47
The Software
The loop() calls two different functions:
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
one for receiving the commands
  Either from Serial (from the ESP8266) or from the IR receiver.
one for the actual driving
Let’s take a look at the configuration file

## Slide 48
The Software
The loop() calls two different functions:
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
one for receiving the commands
  Either from Serial (from the ESP8266) or from the IR receiver.
one for the actual driving

## Slide 49
The Software
Just overvieweing a couple of things in the code, we can see that the init_xyz() we called in the setup() look similar to each other: we use the pinMode() command to set some specific GPIO pins (described in the conf.h) to act either as INPUT or OUTPUT.
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
Other functions use the previously set pins to send digital signals (HIGH/LOW) (5V/0V) with functions like digitalWrite() that’s used to define a state of a GPIO pin when set as OUTPUT

## Slide 50
The Software
Sometimes we may need to output an arbitrary voltage between 0V and 5V, that’s the case when we’re trying to encode a speed for the car, how is it done?
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
We can reproduce an arbitrary voltage between 0 and 5V by rapidly switching a digital pin and then observing a time average: by changing the duty cycle of our fast switching signal i.e. the ratio between the time the signal’s HIGH and the time the signal’s LOW we can reproduce an arbitrary voltage.
This technique is called Pulse Width Modulation

## Slide 51
The Software
We can theoretically implement our PWM routine but that has a big disadvantage: the output signal depends on what the processor is doing and we can’t focus on other operations than producing the PWM signal
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
We can indicate the duty cycle as an int between 0 and 255
To overcome this, Arduino has some PWM-enabled pins that can be controlled using the analogWrite() function without consuming precious controller cycles:

## Slide 52
The Software
The guide step is done without using too many delays because we can’t afford to leave the controller idle a long period of time if we want it to be reasonally reactive: the longest routines have to be implemented using a time reference that’s given by the millis() function
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
We can use it to start timers and to control the duration of a certain operation.
millis() returns the number of milliseconds that have passed from the controller’s bootup.

## Slide 53
The Software
The automatic mode implements really simple logics based on the perceived distances between the car and surrounding objects: these are measured using the HSR04 module.
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
If there’s an echo, the HSR04 sends an HIGH signal whose duration is the same as the time between the signal start and the echo receiving
We’ve written a simple routine to drive the module: we first tell the HSR04 to send a signal on the transducer with a digitalWrite() for 15 ms, then wait for an echo.

## Slide 54
The Software
We can measure the length of a pulse using the pulseIn() function: if it’s set on HIGH it waits for the argument pin to switch from LOW to HIGH and, waits for it to return to LOW and then returns the HIGH time duration.
https://github.com/filippocastelli/uolli
Our Arduino Sketch:

## Slide 55
The Software
The rest of the Arduino code is quite self explanatory and going in detail would take too much time.
https://github.com/filippocastelli/uolli
Our Arduino Sketch:
but that is left as an exercise to the reader
You may also want to check the ESP8266 code that basically creates an HTML page with some interactive buttons, detects the button presses and sends values to serial depending on which button has been pressed.

## Slide 56: Concluding these slides:
What have we learned from this?
Making something actually work can be rewarding
  It’s more rewarding when it doesn’t catch fire
You shouldn’t buy the cheapest part if you want to finish you projects on time
Documentation is everything: if you don’t know what you’re doing you should always go for the most documented solution.
Buy the cheapest parts if you want to learn something in the process
  but you should also consider investing in a Chinese course if you choose this disgraced path.
Look online when you have a problem: someone probably had it before you.
It’s ok to be cheap/lazy: justifying your bad habits can lead you to some new knowledge
Don’t short power rails a week before Christmas: replacements for you fried controllers may take forever to arrive.

## Slide 57: Thanks for your attention!
https://github.com/filippocastelli/uolli